## Slide 1
Z80 ROMLESS SBC / DESIGN OVERVIEW
Classic CPU. Modern I/O controller. No ROM.
A real Z80 runs CP/M from SRAM; the Pico 2 W supplies the infrastructure around it.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
01
TERMINALS
Browser over Wi-Fi
USB serial fallback
+ supervisor commands
PICO 2 W
Multicore I/O controller
Core 0: Z80 control + I/O
Core 1: USB, storage + Wi-Fi
PIO0 matrix; PIO1 bank select
GENERATES THE 20 MHz Z80 CLOCK
Z80 CPU
Executes CP/M and applications
128 KiB SRAM
2 banks; 64 KiB Z80 window
I/O
The Pico is not emulating the Z80. The Z80 directly addresses SRAM and executes every Z80 instruction.
Notes: The memory arrow is a direct Z80/SRAM path. The Pico/Z80 arrow represents virtual I/O and boot/control, not memory bus mastering. Core 0 generates CLK using PWM through the AHCT244 buffer. Implementation evidence (repository-relative paths): src/stage09_flash_storage/main.c src/stage10_websocket_terminal/CMakeLists.txt src/common/cpu.c src/common/clock.c src/common/sram.c The deck describes the current source architecture, not a new hardware qualification. The configured nominal Z80 clock is 20 MHz. Combined networked operation requires timing and acceptance evidence. All diagrams use editable native PowerPoint shapes and text.

## Slide 2
Z80 ROMLESS SBC / DESIGN OVERVIEW
Three hardware building blocks
CPU and SRAM handle execution. The Pico and fixed logic provide a safe, buffered interface.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
02
Z80 + SRAM
Z84C0020PEC Z80
128 KiB SRAM; two 64 KiB banks
GP8→U4 selects SRAM A16; Z80 owns A0-A15 and all writes.
Logic + translation
3.3 V Pico / 5 V CPU interface
AHCT / LVC bus buffers
HCT32 generates hardware WAIT and gates SRAM / data-path enables.
Pico 2 W
RP2350 dual-core controller
Onboard Wi-Fi + USB
4 MiB flash: Pico firmware, boot
image, journal, ENV and disks A:-D:.
Pico PWM / PIO1 → AHCT244 level buffer → Z80 CLK: 20 MHz nominal
Notes: The eight active packages are Pico 2 W, Z80, AS6C1008 SRAM, HCT32, AHCT244, AHCT245, LVC245 and LVC244. SRAM A16 is LOW. Pico never drives A0-A15 or writes SRAM directly. Drives A:-D: each occupy 320 KiB with 128-byte records. Current prototype is breadboard-first; the older PCB is not the current circuit. No SD card, PSRAM or address expander. Implementation evidence (repository-relative paths): src/common/include/z80sbc/pins.h src/common/include/z80sbc/flash_layout.h src/common/bus.c src/common/clock.c docs/docs/en/system/operation.md The deck describes the current source architecture, not a new hardware qualification. The configured nominal Z80 clock is 20 MHz. Combined networked operation requires timing and acceptance evidence. All diagrams use editable native PowerPoint shapes and text.

## Slide 3
Z80 ROMLESS SBC / DESIGN OVERVIEW
Two cores, separated responsibilities
Core 0 serves the Z80. Core 1 owns USB, Wi-Fi and external interfaces.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
03
CORE 0
Z80 control + I/O
Clock generation and reset
SRAM loading and verification
I/O traps and PIO1 bank select
Queued Z80 control requests
SHARED BOUNDARY
Console + diagnostic rings
Supervisor command queue
Disk / service mailboxes
Flash-safe handshakes
CORE 1
USB + storage + networking
USB setup, IRQs and console
Disk-first storage / service workers
Wi-Fi, HTTP + WebSocket
SNTP, weather and chat clients
PIO0 I²C for HT16K33 matrix
100 kHz: GP26 SCL, GP22 SDA
Core 0 never accesses USB endpoints. Core 1 requests Z80 actions through queues, not bus GPIO.
Notes: Stage 10 compiles the Stage 9 automatic-loader main.c with Z80_STAGE10_NETWORK and Z80_STAGE09_AUTOBOOT enabled. RP2350 system clock is set to 120 MHz. Core 1 owns USB initialization, the default alarm pool, USB IRQ/background work, terminal input/output, ANSI mapping and supervisor framing. It starts before boot loading and registers for flash lockout; runtime workers remain gated until verified CP/M startup. A four-entry command queue requests Z80 actions on core 0. All stdout routes into a 4 KiB diagnostic ring with explicit overflow counts; only core 1 drains it to USB. Core 0 never waits on a USB stdout mutex. Core 1 services disk and extended workers before USB/network service. Wi-Fi uses pico_cyw43_arch_lwip_poll. Console rings are RX 128 B / TX 512 B. Timers and immediate port operations remain on core 0. Implementation evidence (repository-relative paths): src/stage09_flash_storage/main.c: core1_main(), start_cpm(), main() src/stage09_flash_storage/usb_console.c src/stage10_websocket_terminal/network_runtime.cpp src/stage10_websocket_terminal/network_services.c src/stage10_websocket_terminal/web_terminal.cpp src/common/terminal_queue.c src/common/io_service.c The deck describes the current source architecture, not a new hardware qualification. The configured nominal Z80 clock is 20 MHz. Combined networked operation requires timing and acceptance evidence. All diagrams use editable native PowerPoint shapes and text.

## Slide 4
Z80 ROMLESS SBC / DESIGN OVERVIEW
Booting without a ROM chip
The Pico supplies instructions; the Z80 uses those instructions to populate its own SRAM.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
04
1
Validate
Start USB core 1.
Recover journal.
Check image CRCs.
2
Load SRAM
Slow-clock Z80.
Inject instructions.
CPU writes 64 KiB.
3
Verify
Read all bytes back.
Compare with flash.
Hold CPU in reset.
4
Start
Arm I/O; reset Z80.
Start 20 MHz clock.
Enable workers.
5
Execute
Fetch from SRAM.
BIOS starts CP/M.
CCP starts programs.
Pico injects LD HL,nn / LD (HL),n for loading and LD A,(HL) for read-back.
After reset: SRAM[0000h] = JP FD00h → BIOS cold entry → CCP. No USB, Wi-Fi or browser required.
Notes: Core 1 starts first, initializes USB and participates in SDK flash lockout during journal recovery. Core 0 completes loading and independent read-back before enabling runtime workers. During injection, SRAM read output is inhibited, but the Z80 still generates all addresses and SRAM writes. z80_cpu_release_reset_and_run resets the CPU with six slow clock cycles, enables SRAM reads, releases RESET and starts PWM after the required settling interval. Load/CRC/verify failures hold RESET LOW. USB remains on core 1 throughout loading and while stopped. The normal execution path has both Pico data paths isolated except during trapped I/O. Implementation evidence (repository-relative paths): src/common/flash_backend.c: load_boot_image() src/common/sram.c: load_hl(), z80_sram_write_byte(), z80_sram_read_byte() src/common/cpu.c: z80_cpu_release_reset_and_run() src/stage09_flash_storage/main.c: load_image(), start_cpm() The deck describes the current source architecture, not a new hardware qualification. The configured nominal Z80 clock is 20 MHz. Combined networked operation requires timing and acceptance evidence. All diagrams use editable native PowerPoint shapes and text.

## Slide 5
Z80 ROMLESS SBC / DESIGN OVERVIEW
Normal execution is direct. I/O is virtual.
The Z80 runs directly from SRAM. PIO1 handles bank-select OUT 07h at hardware speed.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
05
Z80 + SRAM
Ordinary instruction fetches
and memory reads / writes
need no Pico software.
Bank select + I/O traps
Hardware WAIT holds I/O.
Stop clock; transfer byte.
Step cycle; resume PWM.
Virtual peripherals
Console → USB or browser
Disks → onboard flash
Services → async workers
IN / OUT
Console ownership
One browser owns CP/M while connected; USB is the fallback.
Persistent storage
Fast reads on core 0; queued writes / flash commits on core 1.
Runtime flash programming pauses the Z80 through a bus-grant handshake; the Pico still never masters SRAM.
Notes: HCT32 produces WAIT# = IORQ# OR IO_RELEASE. Core 0 stops PWM, validates controls and selects the data path. It raises IO_RELEASE only once the byte path is configured, slow-steps until IORQ and strobe release, isolates both paths, lowers IO_RELEASE and resumes PWM. Trapped port adapters do bounded work, not network calls. Console is data/status 00/01h; disk is 10-14h; framed services are 02-04h. Console handover clears queues. Firmware also retains output-ACK and heartbeat handling in web_terminal.cpp. Disk fast reads use flash/cache synchronously; writes and flushes are immutable queue requests serviced by core 1. Programming requires a core-0 bus-grant handshake and SDK flash-safe execution. Implementation evidence (repository-relative paths): src/common/io_trap.c src/common/disk_device.c src/common/flash_backend.c src/common/terminal_queue.c src/common/io_ports.c src/stage10_websocket_terminal/web_terminal.cpp The deck describes the current source architecture, not a new hardware qualification. The configured nominal Z80 clock is 20 MHz. Combined networked operation requires timing and acceptance evidence. All diagrams use editable native PowerPoint shapes and text.

## Slide 6
Z80 ROMLESS SBC / DESIGN OVERVIEW
The design in three ideas
A small hardware system with clear boundaries between execution, I/O and connectivity.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
06
01
Real Z80 execution
CP/M and applications run on the Z80, directly from SRAM.
02
Pico as the multicore I/O controller
Core 0 handles the Z80; core 1 owns USB, storage and networking.
03
ROMless, self-loading memory
The Pico loads and verifies SRAM. PIO1 selects either 64 KiB bank without changing the 20 MHz clock.
No ROM chip. No Z80 emulation. No Pico memory-bus mastering.
Notes: This deck is deliberately high-level; the detailed architecture SVG remains the engineering companion. Sources are recorded per slide in speaker notes. Stage 10 includes weather and chat clients as independent asynchronous network services, not dependencies of the terminal or Z80 trap. FS_SERVER is stored configuration only, not an implemented remote filesystem. The nominal 20 MHz clock is a firmware configuration, not a claim of combined network hardware qualification. Implementation evidence (repository-relative paths): docs/docs/en/images/system-architecture.svg src/stage10_websocket_terminal/CMakeLists.txt src/stage09_flash_storage/main.c src/stage10_websocket_terminal/network_runtime.cpp src/stage10_websocket_terminal/network_services.c The deck describes the current source architecture, not a new hardware qualification. The configured nominal Z80 clock is 20 MHz. Combined networked operation requires timing and acceptance evidence. All diagrams use editable native PowerPoint shapes and text.

## Slide 7
Z80 ROMLESS SBC / DESIGN OVERVIEW
The processors and memory
Three devices do the work: the Z80 executes, SRAM stores, and the Pico orchestrates.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
07
A1 / CONTROLLER
Pico 2 W
RP2350 dual-core module
01
Core 0: Z80 control
Clocks/resets CPU; PIO1 bank switch; injects/verifies SRAM.
02
Core 1: external I/O
Owns USB, Wi-Fi, flash disks, services and PIO0 I²C display.
03
Supervisor, not CPU
Does not emulate the Z80 or drive A0-A15 / SRAM writes.
U1 / PROCESSOR
Z80 CPU
Z84C0020PEC
01
Executes the software
Runs Z80 instructions, BIOS, CP/M and applications directly from SRAM.
02
Owns memory addressing
Alone drives A0-A15 and performs the actual SRAM read/write cycles.
03
Loads itself by running
Executes Pico-injected loader instructions, then starts from address zero.
U2 / WORKING MEMORY
Static RAM
AS6C1008-55PCN
01
1 Mbit storage
128 KiB x 8 static RAM; retains data while powered.
02
Two 64 KiB banks
PIO1: GP8→U4→A16; R24 pulls GP8 LOW at startup.
03
Program memory
Z80 sees one 64 KiB window; OUT 07h selects the other bank.
At boot, the Z80 writes SRAM using Pico-injected instructions. The Pico compares every read-back byte.

## Slide 8
Z80 ROMLESS SBC / DESIGN OVERVIEW
Fixed logic makes the bus behave
Two simple 5 V logic ICs shape safe clock, memory and I/O control signals.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
08
U3 / FIXED LOGIC
Quad OR gate
SN74HCT32N
01
Three gates are used
Fixed combinational logic; the fourth gate is unused.
02
Wait and SRAM reads
Combines IORQ# / IO_RELEASE for WAIT# and RD# / boot inhibit for SRAM OE#.
03
Data-path enable
Combines RD# with the Pico request to control DATA_UP_OE#; no software or programming.
U4 / CLOCK AND CONTROL BUFFER
Octal buffer
SN74AHCT244N
01
3.3 V to 5 V logic
AHCT inputs recognize Pico and Z80 TTL levels; outputs drive 5 V logic.
02
Clock and bus request
Buffers Pico clock and BUSREQ# to the Z80.
03
Memory controls
Buffers memory controls and level-shifts GP8 bank select to SRAM A16.
U4 provides drive and level translation; U3 makes the fixed active-low control decisions.

## Slide 9
Z80 ROMLESS SBC / DESIGN OVERVIEW
Bus interfaces: one direction, one purpose
The three bus-interface chips keep 5 V signals away from Pico GPIOs and isolate data drivers.
Stage 10 implementation | Current breadboard architecture | 24 October 2026
09
U7 / 5 V MONITOR TO PICO
Octal input buffer
SN74LVC244AN
01
Eight monitored signals
BUSACK#, IORQ#, RD#, WR#, A0-A2 and A4.
02
5 V tolerant input
Runs at 3.3 V and presents safe logic levels to the Pico.
03
GPIO protection
All monitored CPU signals pass through U7 before reaching Pico pins.
U9 / PICO TO Z80 DATA
Fixed-direction transceiver
SN74AHCT245N
01
Drives D0-D7 toward CPU
Carries injected loader bytes and Pico-supplied I/O read data onto the 5 V bus.
02
A-to-B direction
Direction pin is fixed; the Pico never takes over the address bus.
03
Controlled enable
U3 enables the path only for valid Z80 read cycles.
U10 / Z80 TO PICO DATA
Fixed-direction transceiver
SN74LVC245AN
01
Reads D0-D7 toward Pico
Captures SRAM read-back and Z80 I/O write data.
02
5 V to 3.3 V
LVC inputs tolerate the 5 V bus and translate data for Pico GPIOs.
03
Separate output enable
GP7 controls the path; keep it off whenever U9 drives the data bus.
Active inventory: Pico 2 W plus U1, U2, U3, U4, U7, U9 and U10. U5/U6/U8 are not fitted; D1 is a diode.